## Slide 1
Vehicle Detector
Vehicle Detector is a mechanism coupled with LDR and IR works synchronously to detect the arriving vehicle.
IR sensor works on the principle of Infrared light but this ineffective during day time under direct sunlight whereas LDR resistor reacts on intensity of light which is ineffective at night time as there will be no light throughout.
Therefore at day time LDR will be active placed on the surface of the road and as the car arrives the intensity of light will change as the cars shadow will fall on the sensor
And at night time IR will be active such that there will be a transmitter placed at one end of the road and receiver on other end, in this way as the vehicle arrives it will block the lights fired by the transmitter and receiver will not receive any light.
In this way we can detect the car during day as well as night time.
It was also possible to detect the vehicle on camera itself but it will require lot of processing power on long term.
LDR
IR Transmitter
IR Receiver
Speed Breaker to slower the vehicle

## Slide 2
Image Capture
When the front of any vehicle arrives at vehicle detector the vehicle detector becomes active indicates the vehicle has arrived at the vehicle detector. This action will trigger the camera which is placed few feet's ahead of vehicle detector to capture the front of vehicle.
As the vehicle leaves the Vehicle detector becomes inactive indicates the vehicle left the vehicle detector. This action will trigger the camera which is placed few feet’s before the vehicle detector to capture the rear side of vehicle
Camera to capture front side
Camera to capture rear side

## Slide 3
The Pollution check sensor will be placed under the road near the vehicle exhaust area, the position will be 1-3 feets before the vehicle detector’s LDR is placed.
To make it effective following arrangement can be made
  There will be a fan pulling the exhausted air of vehicle which is placed below the metal net.
  This metal net will be parallel to road and will be placed on the surface of road
  The air pulled by the fan will directly be thrown on the PUC Check sensor which then find the purity of air throw by any vehicle
Pollution check
Side view
Pulling Fan
Pollution Check Sensor
Top view
Car

## Slide 4
Sound check
Every vehicle is assigned some maximum limit of sound it can make, beyond that limit it is illegal to drive such vehicle.
To check the overall sound of a vehicle the system uses a microphone which then calculate the intensity sound rating in decibel, which later could be compare with maximum allowed decibel.
This microphone is also placed on the surface of the road right after the speed breaker ends where most of the vehicles accelerate which gives more advantage to sense the intensity of sound
Micophone

## Slide 5
Finding Weight
Over weighted vehicle are not only illegal but they are also harmful on roads.
Since the length and number of axles of all vehicles are not same especially in case of trucks a universal way to calculate weight of all such vehicles on each axle needs to be implemented.
Therefore we came across a solution to create a weighing pads of some length and breadth which later can be placed one after other in a array till it fits all large vehicles
This approach helps to find weight of any type of vehicle from two wheeler to multi axels truck.
Once we get the weight of each axle we then can find the total weight of vehicle by adding all those weights.
Also the benefit is every axle is designed to handle some maximum amount of weight therefore if the weight exceeds the system will come to know and alert the security personal
Barrier
Weighing Pads

## Slide 6
Multi lane
There is no limitation on number of road lanes. As the weighing system is able to weight almost all size of vehicles from 2-wheelers bike to 5-axle Trucks.
At some tolls there is dedicated lane for heavy vehicles such as trucks, buses and light vehicles like personal cars. In such where there is certain that a heavy vehicle is not allowed to pass from light vehicle lane in any circumstances we can reduce the total number of weighing pads to reduce cost
Barrier
Barrier
Dedicated lane for only light weight vehicles

## Slide 7
Design of weight pads
S
Surface of road
Weighing Pad
Weight Cells
To calculate weight on each pad (i.e each axle) internally we need to find sum of following 4 weight cells placed at 4 for corners of a weighing pad